Pneumatic pipe rehabilitation packers

---
Pipe repair from inside the pipe
SECTIONAL REPAIR (up to 5 m)
- Wet Method
Ensure traffic safety
       Ensure work safety
       Clean/prepare working site

---
The width of fiberglass = 3,5 x Ø
Length of fiberglass = 3 x Repairing length
Divide the length of Fiberglass on 3 parts
Prepaire Packer
Grease packer with seperation grease
Wrap the Packer 3-times with Strech folie

---
Mix the mixture
Do not exceed 10 l of mixture
Mix component B and A in the ratio 2:1
The consumption = 1,6l/m² of fiberglass

---
Impegnate the upper side of fiberglass
Fold fiberglass and impregnate

---
Fold the fiberglass for the second time and impregnate
Turn around fiberglass and impregnate the rest of the fiberglass

---
Wrap/turn the impregnated fiberglass on the prepaired packer.
Secure the wrapped fiberglass with wire.
Do not tighten the wire!

---
With push rod drive the prepaired packer and impregnated fiberglass into the pipe.
Set the middle of the packer (contact area) to the point in the pipe you want to repair.

---
When everything is prepaired and positioned correctly, inflate the packer.
Compression force will press the impregnated fiberglass on the damaged point.
After curring time, deflate the packer and pull it out.